## Slide 1: Efficient Use of Battery Arrays
Václav Bernášek - ELI ERIC
Building Knowledge on Battery Technologies in Research Infrastructures (RIs)

## Slide 2: Objective of the Training
Discover the potential of battery storage - why it matters, how it works, and where the market is heading.

## Slide 3: What Are the Key Challenges for Research Infrastructures?
Insights from the FlexRICAN Energy Questionnaire
Power quality issues
  Stability and consistency of electricity supply
  Grid reliability concerns
  Risks of interruptions and fluctuations
  Power consumption limits
    Constraints on maximum energy demand
These challenges highlight the need for efficient energy management and advanced storage solutions to ensure stable and reliable operations.

## Slide 4: Selected benefits of battery storage for RIs
Electrical power quality defects mitigation:
  Brownouts
  Blackouts
  Frequency deviation
  Current-voltage phase shift
  Harmonics
Protection of sensitive equipment
Electricity cost reduction
  Depends on the style of electricity ordering
  EU subsidies
Sustainability
Source: Ecole des Mines de Paris

## Slide 5: Motivation for the Training
42% of Research Infrastructures cite lack of information, complexity, or prioritization as key reasons for not implementing battery storage.
(FlexRICAN Energy Questionnaire)
Chart: Battery useful but not scheduled and reason(s) why
| Financing issues | Not explored | Not a priority | Technical complexity or compatibility with the site | No Business Plan available | No internal expertise
Total | 1 | 1 | 2 | 1 | 1 | 1

## Slide 6
Maximizing the efficiency of integrating battery arrays into the energy ecosystem
This work package examines the impact of external power supply on the internal electrical network and explores strategies to adapt to power quality issues from the supplier.
Exploitable results:
  Tool: Presents a schematic for connecting devices in a sequence designed to mitigate power quality issues while simultaneously reducing costs and emissions based on user inputs.
  Webpage: This webpage offers insights from research and questionnaires, practical examples, and a guide to using the tool.
D7
A streamlined energy chain
2.2027
M3
Functional prototype of technology chain (UPS, UPQ, DA, PVP)
3.2026
FlexRICAN WP4.1

## Slide 7
Power output reserves
(% of peak output of
primary reserves)
Electrical storage for power modulation
This work package studies the impact of internal electrical power storage on the external electrical network by joining the primary and secondary reserve mechanisms.
Revenues through ancillary services
Minimizing the costs
D8
Cost models for participation to fast demand-response service systems
2.2027
M4
Procedure and Cost models for large capacity batteries or participation to service systems at one of the participant RI’s
9.2026
FlexRICAN WP4.2
Power output reserves
(% of peak output of
primary reserves)

## Slide 8: What is energy storage
Energy storage is the capture of energy produced at one time for use at a later time.
A device that stores energy is called an accumulator or battery.
  Consumer electronics
  Embedded Vehicle
  Stationary

## Slide 9: Services that can be adressed by energy storage
Stationary grid storage
Source: EASE

## Slide 10: How to define electrical power quality problems
Power output reserves
(% of peak output of
primary reserves)
  Recommendations:
  Electrical power analyzer downstream of the supplier's power supply
  Portable electrical power analyzer

## Slide 11: Available technology for power failure mitigation

## Slide 12: Connection types for battery storage
Source: https://www.kohler-ups.co.uk/
Online UPS
Line-interactive UPS
Offline UPS

## Slide 13: Battery storage - available technology

## Slide 14: Li-ion batteries
Benefits:
  Fulfilling widest requirements
  Longest life
  Cost efficient
  High energy density
  Fast charging
  Most popular – rapid development, economy of scale
Drawbacks:
  Safety concerns
  Environmental impact
  Temperature sensitivity
Source: evfiresafe.com

## Slide 15: Li-ion Safety
Overcharge protection additives
Include thermal management systems, battery management systems (BMS), venting devices, and fire-retardant materials
Include additional protection in the high-voltage system
Redundant in safety systems
Enhanced manufacturing quality and certification processes for overall safety and reliability.
Source: https://ars.els-cdn.com/

## Slide 16: Li-ion recycling
Currently 70% of battery weight is recycled (EU requirement 50%)
Few High value-added materials can be recovered
Current cost of the recycling process: around €1 to €3/kg
Source: Optimization of the Electrochemical Discharge of Spent Li-Ion Batteries from Electric Vehicles for Direct Recycling by Hyunseok Lee, Yu-Tack Kim and Seung-Woo Lee, 2023

## Slide 17: Li-ion price projections and history
Source: BNEF
Source: BNEF

## Slide 18: Market share of batteries
NCA, LFP, NMC all Li-ion technology
Source: Wood Mackenzie Energy Storage Service

## Slide 19: Comparing Other Types of Batteries with Li-ion